Differential Robot Simulator
Deficiencies Redesign
Gabriel Díaz
#121350
ME3082
Prof. Daniel Lozada

---
Deficiencies List
1. Data Structures module was not fully leveraged as a communication interface between modules.
2. Simulator relied on built-in configuration parameters rather than an external configuration.
3. Cause for derivative action instability was not determined.
1. Motor response time was not analyzed.
2. No quantitative stability analysis of the robot was performed.
3. Figures were not analyzed quantitatively.

---
Data Structures & Config
- data_structures.py now contains structs that are passed by reference to object instantiations.
- This ensures that all objects read the same relevant data.
- Project directory now contains a config.yaml file as a user interface.
- User may modify the config file to setup the simulation parameters, including figure sizes.

---
Derivative Action
- The issues with derivative action were resolved.
- The previous control system included an additional derivative in the orientation set point calculation.
- Effectively, the previous controller was PDD2, not PID.
- Derivative action now no longer destabilizes the system.

---
Motor Block Diagram

---
Motor Response
- Motor state space was derived.
- Eigenvalues analyzed for damping type and stability.
- Step input analyzed for transient response, overshoot, peak time, and settling time.
- Instead of constant load, a known damping term proportional to angular velocity was defined.
- S-Plane poles plotted
- Simulation warns if response time is not negligible.

---
Differential System
- At high errors, θe becomes saturated at ±π/2 radians.
- Position analysis may be ignored, simplifying the state space into 2nd order
- At low errors, sin(θ) and tanh(ktye) can be linearized as θ and ktye
- Robot speed is approximately constant.

---
Motor Feedback

---
Differential Feedback

---
No Noise

---
Nominal Noise

---
High Noise

---
Noise Comparisons
Noise Case	Noise Mean / (rad/s)	Noise Deviation / (Wheel Speed multiplier)	Convergence Time / (s)
None	0	0x	10.5
Nominal	0	1x	10.6
High	0	5x	10.9

---
Deficiencies
- The robot is slow at correcting small errors
- PID and tangent constants have not been rigorously tuned
- The simulator does not integrate the motor’s state, though it does raise a warning when transient response is non-negligible.
- The system analyzer does not incorporate the comparator logic of the simulation’s control system.

---
References
- [1] N. S. Nise, "Modeling in the Frequency Domain," in Control Systems Engineering, 6th ed. Hoboken, NJ: Wiley, 2011, ch. 2, pp. 79–84.
- [2] N. S. Nise, "Modeling in the Time Domain," in Control Systems Engineering, 6th ed. Hoboken, NJ: Wiley, 2011, ch. 3, pp. 117–144.
- [3] N. S. Nise, "Time Response," in Control Systems Engineering, 6th ed. Hoboken, NJ: Wiley, 2011, ch. 4, pp. 161–207.
- [4] N. S. Nise, "Stability," in Control Systems Engineering, 6th ed. Hoboken, NJ: Wiley, 2011, ch. 6, pp. 301–322.

---
For more details...